## Slide 1: RFID based activities of daily living recognition
F. Bergeron, K. Bouchard, S. Giroux, S. Gaboury

## Slide 2: Outline
Context
Indoor tracking
Activity modelling
Activity recognition

## Slide 3: Context
Create an assistive smart home
  Security system
  Activity recognition system
  Feedback system

## Slide 4: Context
Non-intrusive technologies
  RFID, NFC, Wi-Fi, …
  Flowmeters, thermometers, pressure plates, …
  Motion detector

## Slide 5: Context
Targeted users
  Elderly
  Persons with disabilities
  Persons with Alzheiner’s disease

## Slide 6: Indoor tracking system
Offline phase (training)
  Divide the smart home into zones (40cmx40cm to 75cmx75cm)
  Collect 50 training data in each zone
  Train a random forest
Online phase
  Collect readings
  Stabilise using a moving average filter
  Classify with the random forest
  Prevent teleportation using zone filters
Notes: Base of the activity recognition system

## Slide 7: Indoor tracking system
190 zones
Zone filter allows movement in 8 directions
  Takes walls in consideration
  May be more than one neighboring zones in a given direction (zones of varying dimensions)
Accuracy of 97%
  10-fold cross-validation
  Random forest of 250 trees

## Slide 8: Activity modelling
The activity recognition system has access to the position of objects
An activity is composed of interactions between 2 objects
  3 types
    SAME – Both objects are in the same zone
    CLOSE – Objects are within X zones of each other, X small
    FAR – When object that were previously CLOSE are separated
Limitations
  Objects need to move at some point
  Sometimes there may be only one object
    Fake objects (consider environmental position as object, ex: kitchen sink)

## Slide 9: Activity modelling
Interaction is composed of:
  2 objects
  Interaction type
  Minimal time
Exemple: Pour water
  2 objects: glass, sink
  Interaction type: SAME
  Minimal time: 5 seconds

## Slide 10: Activity modelling
Interaction composition
Behaviour tree
  Sequence node
    Children are evaluated in order
    All must complete
  Parallel node
    Children are evaluated concurrently
    All must complete
  Any node
    Children are evaluated concurrently
    Only one must complete

## Slide 11: Activity modelling
Notes: Expliquer l’ordre d’évaluation des nœuds
Temps 1: 1, 6, 2 Temps 2: 3 Temps 3: 4 et 5

## Slide 12: Activity recognition
There are many instances of the same object (ex: many cups)
For each interactions, there are many candidates
  One candidate for each possible pair of object
  Evaluated each time the position of one of its object is updated

## Slide 13: Activity recognition
Exemple
  Pouring water into a glass
    3 glasses (A, B, C)
    2 sinks (K, T)
    6 candidate interactions ({A,K}, {A,T}, {B,K}, {B,T}, {C,K}, {C,T})
  Target: 5 seconds with interaction type SAME
    One reading per second

## Slide 14: Activity recognition

## Slide 15: Activity recognition
Many objects can be equivalent for a task
Object taxonomy
  Tree of objects
    Much like in object oriented programing
  Onthology
    Current engine are too slow
Examples:
  Pour water uses a recipient and a sink
  Pour hot water uses a heat resistent recipient and a sink (or a kettle)

## Slide 16: Activity recognition
Activity probability based on the progression of its interactions
  Can be seen as a score
  Can then be combined with any source
    User’s habits
    Time of day
    Machine learning
Activities can be combined using the behaviour tree to form meta-activities

## Slide 17: Conclusion
We describe a system that can achieve activity recognition using only the relative position of objects
Behaviour tree can be used to order interactions or activities
It is important to consider the object categories for flexibility
Activity can easily be described by a non expert with minimal knowledge