## Slide 1: Qualitative Tracking of Objects in a Smart Home
Frédéric Bergeron KÉvin bouchard
Sébastien Gaboury Sylvain Giroux
Bruno Bouchard

## Slide 2: Outline
Context
Goal of this work
Indoor Positioning System
Indoor Tracking System
Future work

## Slide 3: Context
It is predicted that health care costs will continue to grow at a faster rate than the economy for the next decades
Assistive smart home are seen as a solution as they enable aging in place.
Notes: Population is ageing in occidental countries
It’s a big pressure on health care systems.
United Nation predicts that health care related cost will continue to grow faster than economy for the next decades
A solution is to build housing equiped with different kind of sensors, called smart home, to enable elder to age at home, in a safe and assitive environment Next slide for domus

## Slide 4: Context – DOMUS
Domus is a research laboratory on computer science specialized in smart home and cognitive assistance for people with cognitive deficits.
- Full scale smart home
  6 rooms
  Dozens of sensors
  20 RFID antennas
  - Multi-disciplinary lab
  Programmers
  Ergonomists
  Psychologist
Notes: The work I present today took place in the DOMUS laboratory. We specialize on using computer science and a smart home to provide cognitive assistance and monitoring for people in need, like those suffering from Alzheimer’s disease or traumatic brain injury
In the lab, we have a full scale smart home with dozen of sensors, like motion detector, pressure plate, thermal camera, microphones and so on
Not to forget 20 RFID antennas, used in this experiment

## Slide 5: Goal
Final goal  Activities of daily living recognition
Indoor positioning system (IPS)
Indoor tracking system (ITS)
ADL recognition (work in progress)
Notes: The goal of my master thesis is to use RFID to recognise activities of daily living, using data mining techniques. This will later be used in my lab as part of many specialized moniting system. ADL recognition has been achieved with great accuracy in recent years, with many different technologies
But never with RFID and data mining and relative positioning
Another great difference from previous techniques is
We don’t want to track human, we believe we can do ADL recognition only with objects. This way, we can ignore the problems that arises when many person are in the same house. To do the actual recognition, I first needed an ITS, which itself required and IPS.
But before explaining the IPS, …

## Slide 6: Indoor Positioning System – Tracked Object
Plastic bottle
4 tags
Hold at counter height (about 1m)
Notes: First, for both systems, need a special object to rely on
In plastic to avoid interferences at this early developement stage
4 tags facing different directions
Antennas are at 1 meter high, so is the bottle in our tests
For each tag, we have a reading per antenna, a vector of 20 integers We merge to 4 tags into one, keeping only the highest value foreach antenna

## Slide 7: Indoor Positioning System – Zones
20cm x 20cm: kitchen, dining room
60cm x 60cm: bedroom, bathroom
75cm x 75cm: hall, living room
 accuracy ranging from 80% (dining room) to 95% (hall)
Notes: I said I use relative positioning
It means I use zone of different sizes instead of a precise position in coordinate
When building the IPS, dimensions were…
This is an approximative map of the smart home with zones
The big X are my antennas Using a random forest of 250 trees per room, accuracy range from 80% in the dining room to to 95% in the hall

## Slide 8: Indoor Tracking System – Dataset
6 rooms
4 paths per room
10 tries per path
240 tagged paths total
Notes: Now the traking system
As with the IPS, we first designed a dataset to experiment on.
In each room, we created 4 differents paths that were plausible, like taking the bottle from the fridge to the oven.
For each of those 24 path, we collected data 10 times, resulting with 240 paths we can evaluate accuracy on.

## Slide 9: Indoor Tracking System – Metrics
Targeted Zones Found (TZF)
  Percentage of zones found
Notes: To evaluate our accuracy, we needed metrics.

## Slide 10: Indoor Tracking System – Metrics
Targeted Zones Found (TZF)
  Percentage of zones found
Sequential Targeted Zones Found (STZF)
  Percentage of zones found in the right order

## Slide 11: Indoor Tracking System – Metrics
Targeted Zones Found (TZF)
  Percentage of zones found
Sequential Targeted Zones Found (STZF)
  Percentage of zones found in the right order
Levenshtein distance (L dist)
  Edit distance, number of operations needed to make a sequence equal to another

## Slide 12: Indoor Tracking System – Metrics
Targeted Zones Found (TZF)
  Percentage of zones found
Sequential Targeted Zones Found (STZF)
  Percentage of zones found in the right order
Levenshtein distance (L dist)
  Edit distance, number of operations needed to make a sequence equal to another
Euclidiean distance (E dist)
  Split zones found into N segment, take the mean, compute euclidiean distance with the corresponding N targeted zone

## Slide 13: Indoor Tracking System – Raw results
Metric | TZF | STZF | L dist | E dist
Bedroom | 0,333 | 0,196 | 68,275 | 2,578
Bathroom | 0,589 | 0,311 | 70 | 4,804
Hall | 0,538 | 0,347 | 41,975 | 1,287
Kitchen | 0,372 | 0,179 | 101,225 | 3,353
Living room | 0,591 | 0,327 | 95,525 | 2,325
Dining room | 0,114 | 0,057 | 71,175 | 7,101
Average | 0,423 | 0,236 | 74,696 | 3,575
Notes: Roughly, sequential is half as good
L dist is not good, not showing much, aside that sequence are really long, around 60 zones more than the path.
Euclidiean distance shows that when TZF fall, distance increase

## Slide 14: Indoor Tracking System – Raw results
Metric | TZF | STZF | L dist | E dist
Bedroom | 0,333 | 0,196 | 68,275 | 2,578
Bathroom | 0,589 | 0,311 | 70 | 4,804
Hall | 0,538 | 0,347 | 41,975 | 1,287
Kitchen | 0,372 | 0,179 | 101,225 | 3,353
Living room | 0,591 | 0,327 | 95,525 | 2,325
Dining room | 0,114 | 0,057 | 71,175 | 7,101
Average | 0,423 | 0,236 | 74,696 | 3,575
Notes: It’s really low in places with small zone, like kitchen and dining room
Next is a video, of what it looks like

## Slide 15: Indoor Tracking System – Raw results
Notes: So in green we see the real path we followed
When it turns blue, it’s because we correctly identified the zone
As we can see, the object teleport itself everywhere
Really bad
So we hadded filters

## Slide 16: Indoor Tracking System – Filters
Moving Average
Notes: to try to decrease the error rate (and teleportation)
The first one is simply a moving average

## Slide 17: Indoor Tracking System – Moving Average
Notes: This video shows the effect of the moving average on the stability
The object is at h3, and look it move then stop nobody moves it, it’s a static test nobody moves it

## Slide 18: Indoor Tracking System – Filters
Moving Average
Weighted moving average
Notes: Then the weighted moving average, the generalized form of the previous one

## Slide 19: Indoor Tracking System – Weighted Moving Average
Logarithmic distribution
Notes: We used 4 distribution for the weighted moving average
We used n+2 to make sure we are in the smooth part of the log function

## Slide 20: Indoor Tracking System – Weighted Moving Average
Logarithmic distribution
Linear distribution
Notes: Simple decreasing

## Slide 21: Indoor Tracking System – Weighted Moving Average
Logarithmic distribution
Linear distribution
Exponential distribution
Notes: We tested different value for the parameter a that I’ll show in the next slide

## Slide 22: Indoor Tracking System – Weighted Moving Average
Logarithmic distribution
Linear distribution
Exponential distribution
Factorial distribution
Notes: Once again, many a in the next slide

## Slide 23: Indoor Tracking System - Results
 |  | Metric |  |  | 
N | Weight function | TZF | STZF | L dist | E dist
20 | Log | 0,240 | 0,104 | 119,325 | 6,309
30 | Log | 0,288 | 0,121 | 107,375 | 6,203
40 | Log | 0,291 | 0,120 | 101,150 | 6,300
20 | Linear | 0,256 | 0,142 | 165,175 | 6,375
30 | Linear | 0,408 | 0,185 | 141,675 | 6,262
40 | Linear | 0,457 | 0,206 | 108,250 | 5,955
10 | Exp | 0,191 | 0,092 | 122,825 | 6,193
20 | Exp | 0,232 | 0,105 | 119,375 | 6,405
10 | Exp | 0,245 | 0,112 | 128,225 | 6,211
20 | Exp | 0,321 | 0,145 | 114,65 | 6,453
10 | Factorial | 0,211 | 0,107 | 123,425 | 5,105
10 | Factorial | 0,364 | 0,166 | 132,95 | 4,178
10 | Factorial | 0,453 | 0,219 | 137,5 | 3,819
10 | Factorial | 0,487 | 0,246 | 136,625 | 3,865
 |  | Metric |  |  | 
N | Weight function | TZF | STZF | L dist | E dist
20 | Log | 0,240 | 0,104 | 119,325 | 6,309
30 | Log | 0,288 | 0,121 | 107,375 | 6,203
40 | Log | 0,291 | 0,120 | 101,150 | 6,300
20 | Linear | 0,256 | 0,142 | 165,175 | 6,375
30 | Linear | 0,408 | 0,185 | 141,675 | 6,262
40 | Linear | 0,457 | 0,206 | 108,250 | 5,955
10 |  | 0,191 | 0,092 | 122,825 | 6,193
20 |  | 0,232 | 0,105 | 119,375 | 6,405
10 |  | 0,245 | 0,112 | 128,225 | 6,211
20 |  | 0,321 | 0,145 | 114,65 | 6,453
10 |  | 0,211 | 0,107 | 123,425 | 5,105
10 |  | 0,364 | 0,166 | 132,95 | 4,178
10 |  | 0,453 | 0,219 | 137,5 | 3,819
10 |  | 0,487 | 0,246 | 136,625 | 3,865

## Slide 24: Indoor Tracking System - Results
 |  | Metric |  |  | 
N | Weight function | TZF | STZF | L dist | E dist
20 | Log | 0,240 | 0,104 | 119,325 | 6,309
30 | Log | 0,288 | 0,121 | 107,375 | 6,203
40 | Log | 0,291 | 0,120 | 101,150 | 6,300
20 | Linear | 0,256 | 0,142 | 165,175 | 6,375
30 | Linear | 0,408 | 0,185 | 141,675 | 6,262
40 | Linear | 0,457 | 0,206 | 108,250 | 5,955
10 | Exp | 0,191 | 0,092 | 122,825 | 6,193
20 | Exp | 0,232 | 0,105 | 119,375 | 6,405
10 | Exp | 0,245 | 0,112 | 128,225 | 6,211
20 | Exp | 0,321 | 0,145 | 114,65 | 6,453
10 | Factorial | 0,211 | 0,107 | 123,425 | 5,105
10 | Factorial | 0,364 | 0,166 | 132,95 | 4,178
10 | Factorial | 0,453 | 0,219 | 137,5 | 3,819
10 | Factorial | 0,487 | 0,246 | 136,625 | 3,865
 |  | Metric |  |  | 
N | Weight function | TZF | STZF | L dist | E dist
20 | Log | 0,240 | 0,104 | 119,325 | 6,309
30 | Log | 0,288 | 0,121 | 107,375 | 6,203
40 | Log | 0,291 | 0,120 | 101,150 | 6,300
20 | Linear | 0,256 | 0,142 | 165,175 | 6,375
30 | Linear | 0,408 | 0,185 | 141,675 | 6,262
40 | Linear | 0,457 | 0,206 | 108,250 | 5,955
10 |  | 0,191 | 0,092 | 122,825 | 6,193
20 |  | 0,232 | 0,105 | 119,375 | 6,405
10 |  | 0,245 | 0,112 | 128,225 | 6,211
20 |  | 0,321 | 0,145 | 114,65 | 6,453
10 |  | 0,211 | 0,107 | 123,425 | 5,105
10 |  | 0,364 | 0,166 | 132,95 | 4,178
10 |  | 0,453 | 0,219 | 137,5 | 3,819
10 |  | 0,487 | 0,246 | 136,625 | 3,865
Notes: Accuracy increase with n

## Slide 25: Indoor Tracking System - Results
 |  | Metric |  |  | 
N | Weight function | TZF | STZF | L dist | E dist
20 | Log | 0,240 | 0,104 | 119,325 | 6,309
30 | Log | 0,288 | 0,121 | 107,375 | 6,203
40 | Log | 0,291 | 0,120 | 101,150 | 6,300
20 | Linear | 0,256 | 0,142 | 165,175 | 6,375
30 | Linear | 0,408 | 0,185 | 141,675 | 6,262
40 | Linear | 0,457 | 0,206 | 108,250 | 5,955
10 | Exp | 0,191 | 0,092 | 122,825 | 6,193
20 | Exp | 0,232 | 0,105 | 119,375 | 6,405
10 | Exp | 0,245 | 0,112 | 128,225 | 6,211
20 | Exp | 0,321 | 0,145 | 114,65 | 6,453
10 | Factorial | 0,211 | 0,107 | 123,425 | 5,105
10 | Factorial | 0,364 | 0,166 | 132,95 | 4,178
10 | Factorial | 0,453 | 0,219 | 137,5 | 3,819
10 | Factorial | 0,487 | 0,246 | 136,625 | 3,865
 |  | Metric |  |  | 
N | Weight function | TZF | STZF | L dist | E dist
20 | Log | 0,240 | 0,104 | 119,325 | 6,309
30 | Log | 0,288 | 0,121 | 107,375 | 6,203
40 | Log | 0,291 | 0,120 | 101,150 | 6,300
20 | Linear | 0,256 | 0,142 | 165,175 | 6,375
30 | Linear | 0,408 | 0,185 | 141,675 | 6,262
40 | Linear | 0,457 | 0,206 | 108,250 | 5,955
10 |  | 0,191 | 0,092 | 122,825 | 6,193
20 |  | 0,232 | 0,105 | 119,375 | 6,405
10 |  | 0,245 | 0,112 | 128,225 | 6,211
20 |  | 0,321 | 0,145 | 114,65 | 6,453
10 |  | 0,211 | 0,107 | 123,425 | 5,105
10 |  | 0,364 | 0,166 | 132,95 | 4,178
10 |  | 0,453 | 0,219 | 137,5 | 3,819
10 |  | 0,487 | 0,246 | 136,625 | 3,865
Notes: more smooth it is, better it is

## Slide 26: Indoor Tracking System – Filters
Moving Average
Weighted moving average
Blocking neighbour
  Only allow deplacement if the new zone is a direct neighbour to the old zone
Notes: So we added filter, to try to decrease the error rate (and teleportation)

## Slide 27: Indoor Tracking System – Filters
Moving Average
Weighted moving average
Blocking neighbour
  Only allow deplacement if the new zone is a direct neighbour to the old zone
Limiting neighbour
  Only move one zone at a time, in the direction of the newly predicted zone
Notes: So we added filter, to try to decrease the error rate (and teleportation)

## Slide 28: Indoor Tracking System – Limiting Filter
Notes: This video shows the effect of the limiting filter

## Slide 29: Indoor Tracking System – Limiting Filter
 | Metric |  |  | 
Room | TZF | STZF | L dist | E dist
Bedroom | 0,797 | 0,653 | 124,775 | 2,297
Bathroom | 0,886 | 0,660 | 236,350 | 5,732
Hall | 0,814 | 0,711 | 64,800 | 1,218
Kitchen | 0,863 | 0,567 | 248,500 | 3,720
Living room | 0,913 | 0,753 | 207,250 | 2,143
Dining room | 0,496 | 0,233 | 236,400 | 6,696
Average | 0,795 (+0,372) | 0,596 (+0,360) | 186,346 (+111,650) | 3,634(+0,059)
Notes: This table show how greatly the limiting filter increase accuracy.
L dist is bigger because we cross numerous zones that we did not really go but the filter makes it look like we did

## Slide 30: Future work
Increase the IPS accuracy
  By increasing zones sizes in the kitchen and the dining room
Increase the ITS accuracy
  With new filters
Use the ITS for ADL recognition
Notes: Increase zone size, we did, it works great
New filter, we are open to suggestion, but keep in mind we want to do real time tracking

## Slide 31: Thanks
Questions?